## Slide 1: LOGIC VERIFICATION

## Slide 2: Logic Verification What is verification?
Verification is a process used to demonstrate the functional correctness of a design. It is the act of ensuring that the logic design conforms to the specifications.
Also called logic verification or simulation.
Transformation
Verification

## Slide 3: Logic Verification Functional verification
Simulation
  Directed tests
  Constrained random tests
Formal methods
  Model checking
  Equivalence checking
HDL Design
Testbench
Synthesis
Equivalence Checking
RTL
Gates
Spec
RTL
Functional
Verification
Formal
Verification

## Slide 4: Logic Verification Verification VS. Test
Two often confused
Purpose of test is to verify that the design was manufactured properly
Verification is to ensure that the design meets the functionality intent
Specification
Silicon
Verification
HW Design
Net list
Test
Fabrication

## Slide 5: Logic Verification Why do Verification?
Cost of bugs over time
  Bugs found at the block level have little cost
  Bugs found at the system level may effect the time-to-market
  Bugs found after fabrication require an expensive re-spin
  Bugs found by customers can cost hundreds of millions and worst of all – Reputation
In design 60% - 80% time spent in verification

## Slide 6: Logic Verification Who does Verification?
Designers may begin the process
Verification engineers manage and complete the process
Verification engineers may outnumber designers 2-1

## Slide 7: Logic Verification Why is Verification hard?
How do you know when you are done?
How do you know that your specification is complete?
How do you verify the verifier?

## Slide 8: Functional Verification Approaches Overview
Function verification is primarily done via simulation
  Black-Box Approach
  White-Box Approach
  Gray-Box Approach

## Slide 9: Functional Verification Approaches Black-Box
The verifier has access to input, output and device function
Given a set of inputs the verifier checks for correct outputs
To fully verify a black-box you must show that function is correct for all combinations of inputs
Full verification via black-box testing is impractical for any real design

## Slide 10: Functional Verification Approaches while-Box
The verifier has access (and uses) internal signals during verification
This is common during block-level verification
Input vector
Output vector

## Slide 11: Functional Verification Approaches Gray-Box
The verifier has access (and uses) a limited number of internal signals during verification
This is the reality for most verification
Knowing the architecture of the DUT enables you to write better test

## Slide 12: Verification Flow Goals
Ensure conformance with specification
  But avoid false positives

## Slide 13: Verification Flow Key
The verification engineer should not participate in the logic design of the DUT
Designers may not think of all failing scenarios
Verification engineer have a different perspective on the design
Verification engineers must understand the function, but not the implementation

## Slide 14: Verification Flow Do
Talk to the designer to understand the function of the design
Think of situations the designer neglected
Focus on the corner case or exotic scenarios
Focus on concurrent event
Think about the all the pieces of the design you need to verify

## Slide 15: Verification Flow A typical flow
Devise a potential bug
Write a test-case to expose the bug
Run the simulator with the test-case
Check the simulation result
If the test has uncovered a bug
  Verify the bug
  Work with designer to fix the bug

## Slide 16: Verification Flow High level flow
ASIC Spec
Verification
Plan
Testbench
development
RTL
Handoff
Identify
approach
Level of
Verification
Level of
abstraction
Strategy for
correctness
Create
enviroment
Create
Test cases
Run and
Debug tests
Coverage
Goals satisfied
Stop

## Slide 17: Conclusion
Verification is on critical path
Want to minimize verification time
  Using new tools
  methodologies