## Slide 1: TESTBENCH ORGANIZATION

## Slide 2: TESTBENCH Overview
A testbench is HDL code to verify a module
The main purpose of a testbench is to supply input waveform to the design and to monitor its response
Module Instance: Device Under Verification (DUV)
Testbench Module

## Slide 3: TESTBENCH Major Component of a Testbench
Testbench Environment
Input Stimulus
Response Assessment
Verification Utility
Clock
Generation
Interface
Testbench
Design Under Verification

## Slide 4: TESTBENCH Approach: visual inspection
Device under Verification (DUV)
Stimulus
Generator
Testbench File
Waveform Viewer
OR
Text Output

## Slide 5: TESTBENCH Approach: output comparison
Device under Verification (DUV)
Testbench File
Reference
Model
Stimulus Generator
Output
Comparator
Error/Status Messages
“Gold”
Vectors

## Slide 6: TESTBENCH Approach: self checking
Device under Verification (DUV)
Stimulus
Generator
Output
Signals
Input Signals
Testbench File
Output
Checker
Error/Status
Messages

## Slide 7: TESTBENCH Coding
Coding testbench:
  initial block
  Task and function
  System tasks
General approach:
  Use initial block to apply input vector
  Use # delay operator to sequence input changes in time
  Use @ operator to synchronize with clock
  Use $display to show output, print messages
Common variations:
  Write a task (procedure) to do common checking
  Use a separate always block to generate the clock

## Slide 8: CLOCK GENERATION Explicit Method
One period of a clock is generated
Putting this period inside a loop and initializing the clock produces the complete waveform
    #1 clock = 1'b1;
    #1 clock = 1'b0;
    #2 clock = 1'b1;
    #2 clock = 1'b0;
    initial clock = 1'b0;
    always begin
    #1 clock = 1'b1;
    #1 clock = 1'b0;
    #2 clock = 1'b1;
    #2 clock = 1'b0;
    end

## Slide 9: CLOCK GENERATION Toggle Method
The same clock waveform can also be generated using the toggle method
    initial clock = 1'b0;
    always
    begin
    #1 clock = ~clock; // rising
    #1 clock = ~clock; // falling
    #2 clock = ~clock; // rising
    #2 clock = ~clock; // falling
    end

## Slide 10: CLOCK GENERATION Time Unit
The unit for delay (for example: #2) is specified using timescale
The clock period may change by using parameters to represent the delays, instead of hard coding them
'timescale unit/resolution
    define PERIOD 4
    initial begin
    clock = 1'b0;
    forever begin
    #('PERIOD/2)
    clock = ~ clock;
    end
    end

## Slide 11: STIMULUS GENERATION Overview
In addition to clock, the testbench has to produce various other signals that are used as input to the DUT.
These signals, also called stimulus, have to be applied with specific values at specific times
Stimulus are usually generated in an initial procedural block in the testbench. Many ways exist to apply input vector to DUT

## Slide 12: STIMULUS GENERATION Using Synchronous Method(1)
10111011
10111100
00001110
00101101
00001111
11011011
00110010
10101010
input vector
Stimuli Memory
Stimulus Clock
Testbench
Design
I | D
memory
I/O
Control Data

## Slide 13: STIMULUS GENERATION Using Synchronous Method(2)
reg [M:0] input_vectors [N:0] // stimulus memory
reg [M:0] vector; // input vector
initial
begin
  $load_memory (input_vectors, "stimuli_file");
  i = 0;
end
always @(posedge stimulus_clock)
begin
  if(apply_input == TRUE)
  begin
    vector = input_vectors[i];
    design.address <= vector[31:0];
    ...
    design.data <= vector [M:M-31];
    i = i + 1;
  end
end

## Slide 14: STIMULUS GENERATION Using Task Statement
  // task applying an input to cpu's PIs
  task cpu_apply_input;
  input [N:0] vector;
  begin
    cpu.address = vector[0];
    ...
    cpu.data = vector[j];
    ...
    cpu.interrupt = vector[k];
    ...
  end
  endtask
  initial // use the cpu task to apply inputs
  begin #10;
    cpu_apply_input(64'b0); // reset
    ...
    #50;
    cpu_apply_input(v1); // now start input vector sequence #60;
    cpu_apply_input(v2);
    ...
  end

## Slide 15: STIMULUS GENERATION Using Instruction Code

## Slide 16: RESPONSE ASSESSMENT Overview
The general principle in accessing simulation result consists of 2 parts
  The first part monitors the design’s nodes during simulation
  The second part compares the node values with expected value
Comparison method
  Offline(post processing)
    Node value are dumped out to file during simulation
    The the file is processed after the simulation is finished
  On the fly
    Node value are gathered during simulation and are compared with expected value

## Slide 17: RESPONSE ASSESSMENT Offline
Design state dumping in text or VPD to be viewer by a waveform viewer
initial begin
$vcdpluson;
$vcdplusdeltacycleon;
$vcdplusmemon(
simulation_top.dut.core.NVM_0.model.data_memory);
$vcdplusmemon(
simulation_top.dut.core.NVM_1.model.data_memory);
end

## Slide 18: RESPONSE ASSESSMENT On the Fly

## Slide 19: VERIFICATION UTILITY Overview
Every testbench use s utility routines common to other testbench
These utility can take on the form of a module, a task or a function
Some commonly used verification utility routines are a random error generator and an injector, error and warning display routines, and memory loading

## Slide 20: VERIFICATION UTILITY Display Routines(1)
task test_pass;
begin
$display("\n=====> PASS\n\n");
begin
$display ("||||||||||| |||| ||||||| ||||||| ");
$display ("|| || || || || || || ||");
$display ("|| || || || || ||");
$display ("|| || || || || ||");
$display ("||||||||||| |||||||||| |||||| |||||| ");
$display ("|| || || || ||");
$display ("|| || || || ||");
$display ("|| || || || || || ||");
$display ("|| || || ||||||| |||||| ");
$display ("==========================");
end
$finish;
end
endtask

## Slide 21: VERIFICATION UTILITY Display Routines(2)
task test_fail;
begin
$display("\n=====> FAIL\n\n");
begin
$display ("||||||||||||| |||| |||||||||| || ");
$display ("|| || || || ||");
$display ("|| || || || ||");
$display ("|| || || || ||");
$display ("|||||||||||| |||||||||| || || ");
$display ("|| || || || || ");
$display ("|| || || || || ");
$display ("|| || || || ||");
$display ("|| || || |||||||||| |||||||||| ");
$display ("==========================");
end
$finish;
end
endtask

## Slide 22: VERIFICATION UTILITY Memory Loading
// declaration of a 1K 32-bit wide memory
reg [31:0] mem [1023:0];
// transfer data in file image to memory mem
$readmemh ("image", mem, START_ADDR, END_ADDR);